## Slide 1: Hydrogen Production from Methane
Erica Caruso
Courteney Fabbri
Maurice Smith
Anne Serban

## Slide 2: Topics Covered

## Slide 3: Topics Covered
Brief Overview of Process
Previous Issues and Concerns
Safety and Environmental Analysis
Process Controls
Revised Economic Analysis
Pinch Analysis
Transportation Logistics
Notes: Anne

## Slide 4: Brief Overview

## Slide 5: Overall Process Outline: BFD
Notes: Anne

## Slide 6: Final Feed and Product Streams
Feed/raw material consumption:
  High pressure steam: 2,500 lb/hr
  Pipeline natural gas: 28,000 SCFH
Hydrogen production: 33 barrels/hr
High pressure steam production: 2,300 lb/hr
Notes: Anne

## Slide 7: Previous Concerns

## Slide 8: Previous Concerns: General
Centrifugal compressor
  Changed from air compressor to natural gas compressor
On-site desulfurization
  German pipeline gas cannot exceed 3.6 ppm H2S [1]
  3.6 ppm SO2 produced and removed via FeO pellets
H2O recovery in water gas shift section
  32% untreated feed water recovered
Notes: Courteney

## Slide 9: Added Equipment
New process equipment
  SMR section
    C-101: Natural gas compressor
    VLV-101: Pressure reducing valve
      E-101: Waste heat steam generator
  On-site desulfurization section
    R-101: Oxidizer
    V-101: Packed column absorber
  Water gas shift section
    V-102: Knock-out drum
    V-103: Condensate tank
    P-102: Dirty water pump
FeO catalyst
    “SULFATRAP” Gas Sweetening [11]
Notes: Courteney

## Slide 10: Updated Equipment: SMR and WGS
VLV-101: Pressure reducing valve
On-site Desulfurization DESULF
Hierarchy
V-102:
Knock-out
drum
V-103:
Condensate tank
P-102:
Centrifugal single-stage pump
P-101:
Centrifugal single-stage pump
E-101:
Waste heat boiler/steam generator
Notes: Courteney

## Slide 11: Updated Process Features: Natural Gas Sweetening/DESULF Hierarchy
C-101: Natural gas centrifugal compressor
R-101: Catalytic oxidizer
R-102: Packed sulfur absorber
Notes: Courteney

## Slide 12: Added Equipment
New process equipment
  PSA section
    K-101: Feed to PSA Compressor
    K-102: Mid-Stage PSA Compressor
  Pressurization before Storage
    K-103: Compressed Hydrogen Compressor
  Carbon Capture Section
    E-104: Heat Exchanger for Heat Integration
    E-105: Heat Exchanger for Cooling Recycle
Notes: Maurice

## Slide 13
Updated Equipment: PSA and Carbon Capture
Notes: Maurice

## Slide 14: Previous Concerns: Storage
Pressure requirements for storage
  45 Bar
Hydrogen pickup
  Every 2-3 Days
  Additional 20% storage
MEA Storage
  Delivered every 30 days
Pressure Vessels for Hydrogen [13]
Notes: Maurice

## Slide 15: Process Controls

## Slide 16: Process Controls (General)
Controlled Variables
Reactors: Temperature, Pressure, Conversions
Vessels: Level, Pressure, Purities
Manipulated Variables
Outlet flow, Fuel flow rate, Inlet flow
Notes: Erica

## Slide 17: Detailed Process Control: Primary Reformer
Controlled Variables
Temperature and Pressure
Manipulated Variables
Flow and Level
Temp Range: 1400°F-1600°F
Optimum: 1470°F
Notes: Erica

## Slide 18: HAZOP
Notes: Erica

## Slide 19: Environmental and Safety Concerns

## Slide 20: Environmental Analysis
Hazardous gases:
  CO2, CO, H2S, SO2
    CO2: Regulated through EU Emissions Trading System Cap
Directive of the European Parliament and Council on
Industrial Emissions Standards[2]
  CO2: 1.82 Billion allowance cap/year (Germany)
  CO: 44 ppm
  H2S: Minimum rate of desulfurization is 93%
  SO2: 19 ppm
  NOX: 280 ppm
    European Commission Logo [12]
Notes: Anne

## Slide 21: Environmental Analysis
Average hazardous gas emittance:
  CO2: 360 ppm
  CO: 14 ppm < 44 ppm emission standard
  H2S: 99% rate of desulfurization > 93% minimum rate
  SO2: ~1 ppm < 19 ppm emission standard
  NOx = ~0.04 ppm << 280 ppm
    European Commission Logo [12]
Notes: Anne

## Slide 22: Safety Analysis [5] - [10]
Respiratory diseases can be caused by prolonged exposure to H2S, SO2 and NOx
CO and H2S are highly flammable and toxic.
NOx is fatal if inhaled; it corrodes skin and damages eyes.
Repeated expose to CO can cause damage to various organs.
Prolonged exposure to CO2 may cause suffocation.
Repeated exposure to MEA can cause liver and kidney damage.
NFPA Diamond [15]
Notes: Anne

## Slide 23: Process Safety Concerns
Process | Main Safety Concerns
Sulfur Removal Process | Formation of metal oxide fumes when FeO pellets decompose
Steam Reformer | Reformer operates at very high temperature and pressure; Catalyst is harmful if inhaled
Water Gas Shift | Reactors operate at high temperatures
Carbon Capture | Loss of MEA from system due to leaks in pipes or units
Pressure Swing Absorption | Potentially high operating pressure
Notes: Anne

## Slide 24: Process Safety Concerns
Nickel Ceramic catalyst pellets for reformer tubes[14]
Notes: Anne (this is our reformer tube catalyst, Nickel Ceramic Pellets)

## Slide 25: Economic Analysis

## Slide 26: Capital Cost Estimates
CAPITAL COSTS (CC) |  | 
 | Cost ($MM) | 
Inside Battery Limits (ISBL) | 28.28 | 
Off-site Battery Limit (OSBL) | 8.48 | 30% of ISBL
Contingency | 3.68 | 10% (ISBL + OSBL)
Engineering Procurement & Construction Costs (EPC) | 7.35 | 20% (ISBL + OSBL)
Fixed Capital Costs (FCC) | 47.8 | ISBL + OSBL + Contingency + EPC
Working Capital Costs | 7.17 | 15% FCC
Total CC | 55 | 
Notes: Courteney

## Slide 27: ISBL Cost Analysis
-Purchasing and shipping costs of equipment:
-Desulfurization and Reaction section installed cost: $7.55MM
-Carbon Capture and Pressure Swing Adsorption cost : $20.6MM
-Land costs:
-5 acres of land: $350M (Weinheim, Germany)
-Infrastructure
-Cooling tower: $176M
-Bullets for storage: $8.86MM
-MEA Storage : $328M
-Piping (included in equipment)
-Catalysts, and any other material needed:
-Initial fill cost: $1.14MM
-Two stage ion-exchange water treatment: $17.8M/year
Notes: Courteney

## Slide 28: ISBL Cost Analysis
Chart: ISBL
| Equipment | Infrastructure | Initial Fill Costs | Land
Sales | 28.17 | 9.364 | 0.788 | 0.35
Notes: Courteney

## Slide 29: Operating Cost Estimates
COLD:
-Boiler feed water: $9M/year
-Cooling water: $8M/year
HOT:
-Split methane feed stream used in SMR furnace: $170M/year
-Rest of fuel gas utilities: $72M/year
-HP Steam makeup: $26M/year
Pressure changers:
-Electricity: $470M/year

## Slide 30: Operating Cost Estimates
Heating Duties = $268M/year
Cooling Duties = $17M/year
Electricity = $470M/year
Total Operating Costs = $755M / year
Notes: Courteney

## Slide 31: Revenue Estimates
Revenue from Hydrogen: $18MM/year
    Current price of hydrogen in Germany: $11-$13/kg [3]
      ≈ $65-$75/barrel
    Producing 150,000 kg/year ≈ 260,000 barrels/year
Process Recovery Revenue:
    HP steam from BFW: $211M
Germany’s 2030 Climate Action Package
    Germany National Hydrogen Strategy [4] : $335M
Total Revenue = $18.6MM/year
Notes: Courteney

## Slide 32: Variable Cost of Production (VCOP)
Raw materials:
-Pipeline gas: $680M
-Untreated water: $16M
Utilities:
- $755M / year
Consumables:
-Initial fill costs (catalyst, packing, MEA): $1.14MM
Effluent disposal:
-CO2 Credits = $47M/year
Total VCOP = $2.64MM/year
Notes: Erica

## Slide 33: Variable Cost of Production (VCOP)
Chart: VCOP
| Raw Materials | Utilities | Consumables | Effluent Disposal
Column1 | 1056 | 767 | 778 | 47
Notes: Erica

## Slide 34: Raw Materials Cost
Chart: Raw Materials
| Untreated Water | Natural Gas | MEA
Sales | 16 | 680 | 360
Notes: Erica

## Slide 35: Fixed Cost of Production (FCOP)
-Labor includes salaries of employees and managers.
-Maintenance is average, expected plant maintenance
-Overhead are the costs associated with insurance, additional maintenance costs, and maintaining compliance.
Notes: Erica – This is not fixed cost of production

## Slide 36: Net Present Value (NPV) [7-Year MACRS]
NPV 10 Years : $-4.07MM
20 Years : $6.46MM
*Tax rate assumed 35%
Notes: Maurice

## Slide 37: Net Present Value (NPV) [5-Year MACRS]
NPV 10 Years : $-3.28MM
20 Years : $7.25MM
*Tax rate assumed 35%
Notes: Maurice

## Slide 38: Sensitivity Analysis
Notes: Maurice

## Slide 39: Economic Summary
Total Capital Cost: $55MM
Total Operating Cost: $755M
Total Revenues: $18.6MM
NPV after 20 years: $7.25MM
Notes: Maurice

## Slide 40: Future Work
Improve Economics
- Produce larger quantity of hydrogen
- Supply other markets
-Ammonia
- Pay Cash for capital costs
- Avoids interest on equipment costs
- Consider alternatives to hydrogen storage
- Underground storage
Notes: Maurice

## Slide 41: Future Work
More in-depth market analysis
-Determine if there is an opportunity to increase the amount of hydrogen produced
Improving the carbon capture process in order to increase credits from government
Look to sell our carbon dioxide to another process company looking to make methanol from it
Notes: Maurice

## Slide 42: References
[1] https://ec.europa.eu/energy/intelligent/projects/sites/iee-projects/files/projects/documents/redubar_a_register_of_all_gas_regulations.pdf.
[2] https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX:32010L0075
[3] https://www.reuters.com/article/us-energy-eworld/germanys-ewe-to-test-supplying-hydrogen-for-transport-industry-idUSKBN2041X8
[4] https://www.rechargenews.com/transition/minister-germany-should-start-world-s-first-green-hydrogen-tender-next-year/2-1-758073
Notes: Maurice

## Slide 43: References for Safety Analysis
[5] https://www.airgas.com/msds/001013.pdf (CO2)
[6] https://www.airgas.com/msds/001014.pdf (CO)
[7] https://www.airgas.com/msds/001039.pdf (NO)
[8] https://www.airgas.com/msds/001041.pdf (NO2)
[9] https://www.airgas.com/msds/001029.pdf (H2S)
[10]http://msdssearch.dow.com/PublishedLiteratureDOWCOM/dh_0044/0901b80380044789.pdf?filepath=amines/pdfs/noreg/111-01388.pdf&fromPage=GetDoc (MEA)
[15] https://cleanroom.byu.edu/NFPA

## Slide 44: References for Pictures
[11] https://www.chemicalproductsokc.com/sulfurtrap-h2s-removal-gas/
[12] https://en.wikipedia.org/wiki/European_Commission#/media/File:European_Commission.svg
[13] https://www.tenaris.com/en/products-and-services/industrial-and-mechanical/gas-cylinders-and-large-vessels

## Slide 45: Questions?